## Slide 1: Mechanical ventilation: Thinking simple
Micah Long, MD
Anesthesiology & Critical Care
University of Wisconsin
For Audio, go to “Slide Show,” then “Play from Start” with Audio On

## Slide 2: How does a Ventilator ”Think”?
Modes…
or breaths?
Goal - 2.5 breaths = most modes

## Slide 3: The Breaths
Vents deliver breaths. Breaths are put together to create “modes.”
They deliver: Flow or Pressure
For a set: Time or Flow %
On top of: PEEP & FIO2
And are Synchronized via triggers: To patient effort, or not
Goal - 2.5 breaths = most modes
P
F
PEEP
Insp. Time
Variable
Fixed

## Slide 4: The Breaths
Goal - 2.5 breaths = most modes
F
PEEP
P
Vents deliver breaths. Breaths are put together to create “modes.”
They deliver: Flow or Pressure
For a set: Time or Flow %
On top of: PEEP & FIO2
And are Synchronized via triggers: To patient effort, or not
Insp. Time
Variable
Fixed

## Slide 5: The Breaths - Nomenclature
Vents deliver breaths. Breaths are put together to create “modes.”
They deliver: Flow (volume modes, not PRVC) or Pressure (pressure modes & PRVC)
For a set: Time (control modes), or Flow % (support modes)
On top of: PEEP & FIO2
And are Synchronized via triggers: To patient effort (”assist control”), or not (“conventional”)
Goal - 2.5 breaths = most modes
F
PEEP
P
Insp. Time
Variable
Fixed

## Slide 6: The Breaths
Vents deliver breaths. Breaths are put together to create “modes.”
They deliver: Flow or Pressure
For a set: Time or Flow %
On top of: PEEP & FIO2
And are Synchronized via triggers: To patient effort, or not
Goal - 2.5 breaths = most modes
P
F
PEEP
Insp. Time
Variable
Fixed
Repeating for emphasis

## Slide 7: The Breaths
Goal - 2.5 breaths = most modes
F
PEEP
P
Vents deliver breaths. Breaths are put together to create “modes.”
They deliver: Flow or Pressure
For a set: Time or Flow %
On top of: PEEP & FIO2
And are Synchronized via triggers: To patient effort, or not
Insp. Time
Variable
Fixed
Repeating for emphasis

## Slide 8: The Breaths - Nomenclature
Vents deliver breaths. Breaths are put together to create “modes.”
They deliver: Flow (volume modes, not PRVC) or Pressure (pressure modes & PRVC)
For a set: Time (control modes), or Flow % (support modes)
On top of: PEEP & FIO2
And are Synchronized via triggers: To patient effort (”assist control”), or not (“conventional”)
Goal - 2.5 breaths = most modes
F
PEEP
P
Insp. Time
Variable
Fixed
Repeating for emphasis

## Slide 9: Principles of Physics: V=IR
V = IR
V = Pressure gradient I = Flow (L / second) = thus, volume R = Resistance (the opposite of compliance)
Note that Resistance includes both the circuit (tubing, ETT), and the patient (airway, lungs, chest wall and WOB/Effort)
F
PEEP
P
Flow (L/s) * Time (s) = Volume

## Slide 10: Roadmap
Types of Breaths
Pressure Breath
  Support Breath
Flow Breath (volume)
Modes of Ventilation
Trad Control (PC, VC)
Assist Control (PC/AC, VC/AC, PRVC)
Support & SIMV
Non-invasive Modes (different names, same thing)

## Slide 11: Pressure Breath
“Physiologic”
  This is how we breath, except we breath with negative pressure and the vent gives positive pressure
  Both expand the balloon

## Slide 12: Pressure Control Breath
Delivers: Pressure
For a set: Time
On top of: PEEP & FIO2
And can be Synchronized or not
Goal - 2.5 breaths = most modes
F
PEEP
P
Insp. Time
Variable
Fixed
Pressure turns on quickly (“Rise Time”)
AUC=Vt
V=IR: Flow is Variable (thus, tidal volume)
  Applied Pressure V=IR
  Compliance V=IR ETT; Lungs, Chest Wall and WOB/Effort
Decelerating Flow
  Lungs empty = Compliant, Patm (↑∆P)
  Lungs full = Not compliant, Pvent (↓∆P)

## Slide 13: Inspiratory Time Errors: Itime Set Too Long
Pressure Equilibrates
  Lung P = Vent P
V = IR
  No V  No Flow
Downstream Consequences
  Does not cause PTX!
  Use up all breathing time in inspiration - no time left to exhale.
    Air Trap
  Uncomfortable
P
F
↑ ↑ I-Time
PEEP

## Slide 14: Inspiratory Time Errors: Itime Set Too Short
Physics Never Changes (V=IR)
  The Flow-Curve peak and deceleration looks the same.
The flow pattern cuts off early
  Low Tidal Volume. You miss out on a lot of AUC
Downstream Consequences
  Small Vt = Low Vmin
  To get to your goal tidal volume, you have to use a lot of pressure.
  Uncomfortable
P
F
Shorter I-Time
”Missed” tidal volume!
PEEP

## Slide 15: Adjusting Tidal Volume with Pressure Breaths
Delivers: Pressure
For a set: Time
On top of: PEEP & FIO2
And can be Synchronized or not
Goal - 2.5 breaths = most modes
F
P
Insp. Time
Fixing Compliance
Larger ETT (only matters <5.5-6), suction ETT, drain water from tubes.
WOB – unsedate, unparalyze, get stronger. Improve synchrony with right mode & right breath settings.
Position & Recruit – Weight of abdomen off of diaphragm, Prone (ARDS). Optimize PEEP +/- Recruitment Maneuvers.
Treat Underlying Disease – Albuterol, Antibiotics
V = IR

## Slide 16: Pressure Support Breath
These are Synchronized (flow triggered)
Delivers: Pressure
For a set: Flow %
On top of: PEEP & FIO2
Goal - 2.5 breaths = most modes
F
PEEP
P
Flow Cycled
30%
100%
Fixed
Pressure turns on quickly (“Rise Time”)

## Slide 17: Pressure Support Breath
These are Synchronized (flow triggered)
Delivers: Pressure
For a set: Flow %
On top of: PEEP & FIO2
Goal - 2.5 breaths = most modes
F
PEEP
P
Flow Cycled
Fixed
30%
What if the patient coughs?
What if they breath out?
What if they “suck in” for a bigger breath?
How can you get a bigger breath?
The same rules apply! Bigger / Suctioned ETT, Weight off diaphragm, Optimal PEEP/Recruit, Tx Underlying.
On the Vent: Increase P or Change Flow Cycling

## Slide 18: Flow Breaths

## Slide 19
P
F
PEEP
Variable
Fixed
Flow Breath
mL/s
Insp. Time
Delivers: Flow
For a set: Time (flow x time = Vtidal)
On top of: PEEP & FIO2
And can be Synchronized or not
V=IR: Pressure is Variable
  Vent Gives Flow V = I R
  Compliance dictates Pressure V = I R ETT; Lungs, Chest Wall and WOB/Effort
Pressure Depends on Where it is Sensed
  At the Vent
  At the Alveolus – shown here (expanding balloon)

## Slide 20
P
F
PEEP
Variable
Fixed
Flow Breath: Pressure sensed at the vent
mL/s
Insp. Time
Delivers: Flow
For a set: Time (flow x time = Vtidal)
On top of: PEEP & FIO2
And can be Synchronized or not
There is a lot in between the Vent and the Alveolus
Vent
(sensor)
Tubes
ETT
Trachea
Bronchi Bronchioles
Alveolus
If flow-restricting (small space or high flow),
The vent pressure sensor will be falsely high
Peak
Plateau

## Slide 21
Pressure sensor
Alveolus
Tubes, Bronchioles
The faster you blow, or the smaller the straw, the more your cheeks blow up before the balloon

## Slide 22
P
F
PEEP
Flow Breath: Pressure sensed at the vent
Insp. Time
High Peak-Plateau Gradient:
  Anything flow-restricting (small) in between the vent and the alveolus
    Kinked tubes, mucous plug, tracheal mass
    Bronchospasm (bronchioles!)
  This is not dangerous except in severe prematurity
There is a lot in between the Vent and the Alveolus
Vent
(sensor)
Tubes
ETT
Trachea
Bronchi Bronchioles
Alveolus
If flow-restricting (small space or high flow),
The vent pressure sensor will be falsely high
Peak
Plateau

## Slide 23: Adjusting Pressure with Flow Breaths
P
F
Insp. Time
Delivers: Flow
For a set: Time (flow x time = Vtidal)
On top of: PEEP & FIO2
And can be Synchronized or not
Fixing Compliance
Larger ETT (only matters <5.5-6), suction ETT, drain water from tubes.
WOB – unsedate, unparalyze, get stronger. Improve synchrony with right mode & right breath settings.
Position & Recruit – Weight of abdomen off of diaphragm, Prone (ARDS). Optimize PEEP +/- Recruitment Maneuvers.
Treat Underlying Disease – Albuterol, Antibiotics
Peak

## Slide 24
Decelerating flow
P
F
P
F
Insp. Time
Decel Flow (computer driven)
Pressure still variable
Looks more like a Pressure Breath, but the Flow is Fixed and is not related to patient compliance or effort.

## Slide 25: Airway Leak – What mode would you pick?
Flow Breath?
  Fixed Flow, e.g. 500 mL
  That’s all you get!
Pressure Breath?
  Flow varies : compliance
    What is “compliance” in this situation?
    Big hole = “compliant”!
  Get lots of flow with a leak
No cuff
Bronch or Uncuffed ETT
Zoom

## Slide 26: Roadmap
Types of Breaths
Pressure Breath
  Support Breath
Flow Breath (volume)
Modes of Ventilation
Trad Control (PC, VC)
Assist Control (PC/AC, VC/AC, PRVC)
Support & SIMV
Non-invasive Modes (different names, same thing)